## Slide 1: Circuits
I hope you are “open” to learning this material and have the “capacity” to internalize it…

## Slide 2: What is an Electric Circuit?
Circuit: Simply a closed loop through which charges can continuously move.
Electricity is not just present in the “bulb” or resistor but throughout the whole circuit.

## Slide 3: Requirements of a Circuit
A Closed Conducting Path
  Must extend from the positive to the negative.
An Energy Supply
  There must be an electric potential difference across the two ends of a circuit, like a battery.
  How is energy produced in a battery?
    Charge is moved from the low energy terminal (-) to the high energy terminal (+). Work is done on the charge to move it. The electrochemical cell provides the energy to do the work on the charge. This establishes and electrochemical difference across the two ends of the electric circuit.

## Slide 4: Current
Current: the rate at which charge flows past a point in a circuit.
It is a rate quantity: some quantity over time, like velocity.
Current is the quantity of charge over time.
I =Q/t
Units: Ampere or Amp (A)
1 Amp = 1 Coulomb/1 second

## Slide 5: Examples:
A 2mm long cross section of wire is isolated and 20 C of charge is determined to pass through it. What is the current?
0.5 Amps
A 1 mm long cross section of wire is isolated and 2 C of charge is determined to pass through it in 0.5 s. What is the current?
4 Amps

## Slide 6: What direction does current flow?
All negatively charged electrons move in the direction opposite the electric field.
However, charge carriers can be positive, negative charges or both.
The Convention: You can thank Ben Franklin…The direction in which a positive charge would move is the direction of the flow. So, current in a circuit it directed AWAY from the positive terminal and toward the negative terminal.

## Slide 7: POWER:
Power: The rate at which electrical energy is supplied to a circuit of consumed by a load.
Power= Energy consumed by load/time
P = ΔE/t
Unit: is watt (W) (I know same as work)
1 watt = 1 joule/second

## Slide 8: What is a kilowatt-hour?
What Northwest bills us in.
A kilowatt is a unit of power and an hour is a unit of time.
Utility companies charge for using electrical energy.

## Slide 9: Calculating Power:
Power is the rate at which energy is added or removed from a circuit by a battery or a load.
Current is the rate wat which charge moves past a point on a circuit.
Electric Potential Difference across the two end of a circuit is the potential energy difference per charge between these two points.

## Slide 10: We Can Combine all Three Equations!

## Slide 11: Examples:
Determine the ...
a. ... current in a 60-watt bulb plugged into a 120-volt outlet.
b. ... current in a 120-watt bulb plugged into a 120-volt outlet.
c. ... power of a saw that draws 12 amps of current when plugged into a 120-volt outlet.
d. ... power of a toaster that draws 6 amps of current when plugged into a 120-volt outlet.
e. ... current in a 1000-watt microwave when plugged into a 120-volt outlet

## Slide 12: Answers:
A) 0.5 A
B) 1.0 A
C) 1440 W
D) 720 W
E) 8.3 A

## Slide 13: Concepts
An electrochemical cell supplies the energy needed to move a charge from a low potential location to a high potential location
The charge that flows through a circuit originates in the wires of the circuit. The charge carriers in wires are simply the electrons possessed by the atoms that make up the wires
Charge moves abnormally slowly - on average, about 1 meter in an hour - through a circuit. Yet as soon as a switched is turned to ON, charge located everywhere within the circuit begins to move
The rate at which charge flows is everywhere the same within an electric circuit. The rate at which charge flows into a light bulb is the same as the rate at which charge flows out of a light bulb
An electrical appliance such as a light bulb transforms the electrical energy of moving charge into other forms of energy such as light energy and thermal energy. Thus, the amount of electrical energy possessed by a charge as it exits an appliance is less than it possessed when it entered the appliance

## Slide 14: How does an Electron Move?
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 15: Go With the FLOW!
This Photo by Unknown Author is licensed under CC BY-NC-ND

## Slide 16: Common Misconceptions
Batteries are not rechargeable
  No charge is lost in a battery only the energy to move charge, as charge does NOT reside in a battery.
  They supply the energy to move a charge from a low potential location to a high potential location.
  Charge originates in the wires of the circuit, not the battery or source
  “rechargeable” batteries rely on turning chemical products back into chemical reactants.

## Slide 17: Resistance
The hindrance to the flow of charge.
What affects resistance?
  The total length of wires. Longer wire = more resistance.
  Cross-sectional area of the wires. Wider wire = more resistance.
  Wire material. Higher resistivity = more resistance.

## Slide 18: Resistivity of Common Materials
Material | Resistivity(ohm•meter)
Silver | 1.59 x 10-8
Copper | 1.7 x 10-8
Gold | 2.2 x 10-8
Aluminum | 2.8 x 10-8
Tungsten | 5.6 x 10-8
Iron | 10 x 10-8
Platinum | 11 x 10-8
Lead | 22 x 10-8
Nichrome | 150 x 10-8
Carbon | 3.5 x 10-5
Polystyrene | 107 - 1011
Polyethylene | 108 - 109
Glass | 1010 - 1014
Hard Rubber | 1013

## Slide 19: Math of Resistance
Resistance is measured in Ohms and is represented by an Ω.
R = p (L/A)
p = resistivity of the material
L = Length of the wire (in meters)
A = Area of the wire (in meters ^2)

## Slide 20: Ohm’s Law
ΔV = I • R
ΔV = the electric potential difference between two points in a circuit.
I = Current between those two points
R = total resistance of all electrical devices between those two points.

## Slide 21: Seriously Potential Difference!
Potential Difference = VOLTAGE or the Volt

## Slide 22: How to measure Current
Two common tools are used
Ammeter = used to measure current at a given location. It is placed in series.
Voltmeter = a device with probes that can touch to location on a circuit to determine the electric potential difference across those location. Not placed in series.

## Slide 23: All in ONE place!
Quantity | Symbol | Equation(s) | Standard Metric Unit | Other Units
Potential Difference (a.k.a. voltage) | ΔV | ΔV = ΔPE / Q ΔV = I • R | Volt (V) | J / C
Current | I | I = Q / t I = ΔV / R | Amperes (A) | Amp or C / s or V / Ω
Power | P | P = ΔPE / t (more to come) | Watt (W) | J / s
Resistance | R | R = ρ • L / A R = ΔV / I | Ohm (Ω) | V / A
Energy | E or ΔPE | ΔPE = ΔV • Q ΔPE = P • t | Joule (J) | V • C or W • s

## Slide 24: Questions:
A certain electrical circuit contains a battery with three cells, wires and a light bulb. Which of the following would cause the bulb to shine less brightly? Choose all that apply.
a. increase the voltage of the battery (add another cell)
b. decrease the voltage of the battery (remove a cell)
c. decrease the resistance of the circuit
d. increase the resistance of the circuit

## Slide 25: Questions
Use the Ohm's law equation to provide numerical answers to the following questions:
a. An electrical device with a resistance of 3.0 Ω will allow a current of 4.0 amps to flow through it if a voltage drop of ________ Volts is impressed across the device.
b. When a voltage of 120 V is impressed across an electric heater, a current of 10.0 amps will flow through the heater if the resistance is ________ Ω.
c. A flashlight that is powered by 3 Volts and uses a bulb with a resistance of 60 Ω will have a current of ________ Amps.

## Slide 26: Answer:
A) 12 volts
B) 12 Ohms
C) 0.05 Amps

## Slide 27: Question

## Slide 28: Answer
A) R = 3 Ohms
  I = 2 Amps (remember current is the same everywhere)
B) R = 6 Ohms
  V = 6 Volts
C) V = 4 Volts
  I = 2 Amps
D) V = 2 Volts

## Slide 29: Circuit symbols and circuit diagrams

## Slide 30: The Symbols

## Slide 31: The lamp
Lamps or lightbulbs are resistors in circuits.
As such they can be represented with the resistor symbol or the lamp symbol below.

## Slide 33: Drawing a Circuit vs. Schematic of a Circuit

## Slide 34: Series Circuit vs Parallel Circuit

## Slide 35: Set up two circuits
Make a series circuit with three bulbs (resistors) Answer these questions
  As the number of resistors increases, what happens to the overall current within the circuit?
  As the number of resistors increases, what happens to the overall resistance within the circuit?
  If on of the resistors is turned off (light bulb is loosened to go out) what happens to the other resistors in the circuit?
Make a parallel circuit with three bulbs and answer the questions again.

## Slide 36: How to set up your Parallel Circuit

## Slide 37: For a Series Circuit
The more resistors that are added the overall current within the circuit decreases (light bulbs get dimmer)
The decrease in current is consistent with the conclusion that the overall resistance increases.
If one of the three bulbs in a series circuit is unscrewed from its socket, then it is observed that the other bulbs immediately go out. In order for the devices in a series circuit to work, each device must work.

## Slide 38: For a Parallel Circuit
As you add more resistors your indicator bulb should get brighter.
As the number of resistors increases, the overall current increases. This indicates a decrease in the overall resistance in the circuit.
If an individual bulb is unscrewed from its socket the remaining bulbs still work.

## Slide 39: Why does this happen?
We can create an analogy between the flow of traffic in a tollway system to that of charge through a wire.
Tollbooths restrict movement like resistors do in a circuit.
Suppose we add more tollbooths to increase the flow of traffic. If we were to add them on the same street one right after the other what would happen?
Now what would happen if we placed them next to each other?

## Slide 41: Series Circuits
Charge flows together through the circuit at a rate that is everywhere the same. There is no greater current at one location then at another location.
Equivalent Resistance: the amount of resistance that a single resistor would need in order to equal the overall effect of the collection of resistors that are present in the circuit.

## Slide 43: Equivalent Resistance in a Series Circuit
For a series circuit:
  R(eq) = R1 + R2 + R3 + …

## Slide 44: Charge in a Series Circuit
Charge does NOT pile up and being to accumulate at any given location.
Charge does NOT become used up by resistors such that there is less of it at one location compared to another.
Current: the rate at which charge flows
I (battery) = I1 + I2 + I3

## Slide 45: Current Calculated
Current can easily be calculated if the voltage of battery is known and the individual resistance values are known.
REMEMBER OHM’S LAW!!!
I(battery) = I1 + I2 + I3 = ΔV (battery) / R(eq)

## Slide 46: Electric Potential Difference and Voltage Drops
Voltage Drop: Occurs as the electrical energy of the charge is transformed to other forms of energy (thermal, light, mechanical) within the resistors or loads.
There is a voltage drop for each resistor, but the sum of these voltage drops is equivalent to the voltage of the battery.

## Slide 47: So What?

## Slide 48: Mathematical Analysis of Series Circuits

## Slide 49: Parallel Circuits
Current: In a parallel circuit charge divides up into separate branches such that there can be more current in one branch than there is in another.

## Slide 50: Equivalent Resistance

## Slide 51: Equivalent Resistance Mathematically
In parallel circuits: 1/R(eq) = 1/R(1) + 1/R(2) + 1/R(3)…
Try it out…

## Slide 52: Voltage Drop for Parallel Branches
Charge does not pass through every resistor; it passes through a single resistor.
The entire voltage drop across that resistor must match the battery voltage.
Vbattery = V1 = V2 = V3 =

## Slide 53: Mathematical Analysis

## Slide 54: Combination Circuits

## Slide 55: How do you solve?
Treat the Parallel circuit as one resistor and find the equivalent resistance.
Then add it back into the circuit to find the equivalent resistance for a series circuit.

## Slide 56: Give it a try

## Slide 58
a. The current at location A is _____ (greater than, equal to, less than) the current at location B.
b. The current at location B is _____ (greater than, equal to, less than) the current at location E.
c. The current at location G is _____ (greater than, equal to, less than) the current at location F.
d. The current at location E is _____ (greater than, equal to, less than) the current at location G.
e. The current at location B is _____ (greater than, equal to, less than) the current at location F.
f. The current at location A is _____ (greater than, equal to, less than) the current at location L.
g. The current at location H is _____ (greater than, equal to, less than) the current at location I.

## Slide 59
A) Equal
B) Greater Than
C) Less Than
D) Greater Than
E) Greater Than
F) Equal to
G) Less Than